## Slide 1
https://github.com/SmartX-Labs/SmartX-Mini-MOOC
Lab #1: Box
Computer Systems
For AI-inspired Cloud
Theory & Lab.

## Slide 2
Box Lab: Outline
eth0
br0
VM
Container
Tap1
ping test

## Slide 3
VM
Box Lab: Final Goal

## Slide 4
The keyboard means that you should execute instructions by following the guidance.
Lab Theory
Lab
Practice
Lectures are divided into Lab Theory, Lab Practice and Lab Review parts.
Lab
Review
Before you start
- Things you need to know

## Slide 5
Lab Theory

## Slide 6
eth0
br0
VM
Container
Tap1
ping test
Linux Box with Virtualization/Containers
Virtual Machine
&
Container
Linux Box

## Slide 7
Virtual Machines (VMs)
Heavier than
Container!
Hypervisor Tool for creating VMs
On a Linux Box (e.g., NUC)
Multiple fully-isolated (with dedicated resources), but heavy VM instances (i.e., VMs).
Multiple partially-isolated, lightweight container instances (i.e., containers)
VMs and Containers on a Linux Box
Containers
Container Runtime Tool for running containers

## Slide 8
eth0
br0
VM
Container
Tap1
ping test
A Switch inside Linux Box: Open vSwitch

## Slide 9
Hypervisor
VM
Virtual switch
VM
VM
VM
Physical switch
Virtual NIC
Virtual interface
Virtual L2 network
Linux Box
L2 network
A software-based virtual switch allows one VM to communicate with neighbor VMs as well as to connect to Internet (via physical switch).
Software-based switches (running with the power of CPUs) are known to be more flexible/upgradable and benefited of virtualization (memory overcommit, page sharing, …)
VMs (similarly containers) have logical (virtual) NIC with virtual Ethernet ports so that they can be plugged into the virtual interface (port) of virtual switches.
Virtual Switch in a Box to connect VMs

## Slide 10
http://openvswitch.org/
Open vSwitch is an open-source virtual switch software designed for virtual servers.
OVS Main components
Linux-adopted virtual switch: Open vSwitch

## Slide 11
Lab Practice

## Slide 12: NAME: NUC5i5MYHE (NUC PC) CPU: i5-5300U @2.30GHz CORE: 4 Memory: 16GB DDR3 HDD: 94GB
#0 - Lab Preparation
Wired connection
NAME: Raspberry Pi Model B (Pi) CPU: ARM Cortex A7 @900MHz CORE: 4 Memory: 1GB SD Card: 32GB
NAME: netgear prosafe 16 port gigabit switch(Switch) Network Ports: 16 auto-sensing 10/100/1000 Mbps Ethernet ports
NAME: NT900X3A
CPU: i5-2537U @1.40GHz
CORE: 2 Memory: 4GB DDR3 HDD: 128GB

## Slide 13
OS : Ubuntu Desktop 16.04.4 LTS(64bit)
  Download Site : http://old-releases.ubuntu.com/releases/16.04.4/
    Bootable USB configuration (no bootable CD, no CD-Rom in NUC) using the downloaded file (ubuntu-16.04.4-desktop-amd64.iso, 1.5Gb)
    Installed on NUC
Ubuntu Home Screen After Installation
#1 - NUC: OS Installation

## Slide 14
#2 - NUC: Network Configuration (1/4)
eth0
br0
VM
Container
Tap1
ping test

## Slide 15
$sudo vi /etc/network/interfaces
----------------- /etc/network/interfaces -----------------
auto lo
iface lo inet loopback
auto eth0
iface eth0 inet static
address [ip address]
netmask [subnet mask]
gateway [gateway]
dns-nameservers [nameserver 1] [nameserver 2]
----------------------------------------------------------------------------
Do not check ‘Enable Networking’
$sudo ifdown eth0
$sudo ifup eth0
NUC internet works!
#2 - NUC: Network Configuration (1/4)
- eth0 interface
Your Box
eth0
203.237.x.x

## Slide 16
eth0
br0
VM
Container
Tap1
ping test
#3 - NUC: OVS installation

## Slide 17
$sudo apt-get update
$sudo apt-get install openvswitch-switch
Update index information of Open vSwitch package.
Install a Open vSwitch package, openvswitch-switch.
Other dependencies are automatically installed.
#3 - NUC: OVS installation
- Update installation of OVS package

## Slide 18
eth0
br0
VM
Container
Tap1
ping test
#4 - NUC: Network Configuration (2/4)

## Slide 19
Modify network interface configuration.
$sudo vi /etc/network/interfaces
----------------- /etc/network/interfaces -----------------
# The primary network interface
auto eth0 # Append this line
iface eth0 inet manual # Append this line
auto (eth0->)br0
iface (eth0->)br0 inet static
…
before
After
Some NUC have different Interface name.
So you need to check your NUC’s interface name using
‘ifconfig’ command.
Don’t reboot or issue “ifup” or “ifdown” command
until the bridge operation is completed.
#4 - NUC: Network Configuration (2/4)
- Register OVS br0 in NUC

## Slide 20
eth0
br0
VM
Container
Tap1
ping test
#5 - NUC: Network Configuration (3/4)

## Slide 21
$sudo OVS-vsctl add-br br0
#5 - NUC: Network Configuration (3/4)
- Connect OVS br0 and NUC eth0 via OVS

## Slide 22
$sudo OVS-vsctl add-port br0 eth0
eth0 인터페이스가 global 영역에서 bridge 영역으로 이동하기 때문에 연결이 끊김
#5 - NUC: Network Configuration (3/4)
- Connect OVS br0 and NUC eth0 via OVS

## Slide 23
$sudo ip route flush table main // Removing routing table of OS
$sudo ip addr flush dev eth0 // Removing the IP address of eth0
$sudo ip addr flush dev br0 // Removing the IP address of br0
$sudo ifup br0 // Turning on “br0” interface
$sudo ip link set eth0 up // Turning on “eth0” interface
#5 - NUC: Network Configuration (3/4)
- Connect OVS br0 and NUC eth0 via OVS

## Slide 24
Your Box
Your Box
eth0
br0
203.237.x.x
eth0
203.237.x.x
#5 - NUC: Network Configuration (3/4)
- Connect OVS br0 and NUC eth0 via OVS
Note: After OVS setting, later we will create VM and connect it.
Your Box
eth0
br0
203.237.x.x
VM 203.237.x.x

## Slide 25
VM
KVM-based VM connected via OVS
- Goal of this section

## Slide 26
eth0
br0
VM
Container
Tap0
ping test
#6 - NUC: Network Configuration (4/4)

## Slide 27
Let’s make a tap interface and attach it to your VM.
$sudo vi /etc/network/interfaces
----------------- /etc/network/interfaces -----------------
…
(Append the lines below to the config file)
auto tap0
iface tap0 inet manual
pre-up ip tuntap add tap0 mode tap
up ip link set dev tap0 up
post-down ip link del dev tap0
#6 - NUC: Network Configuration (4/4)
- Connect OVS tap0 & br0 through OVS

## Slide 28
Your Box
eth0
br0
203.237.x.x
VM
203.237.x.x
tap0
We should make VM attaching tap0. You can think this tap as a NIC of VM.
$sudo ifup tap0
$sudo OVS-vsctl add-port br0 tap0 // Turn on and attach to br0
Turn on the tap interface and attach it to br0.
[tap_name]
#6 - NUC: Network Configuration (4/4)
-Connect tap0, br0 through OVS

## Slide 29
eth0
br0
VM
Container
Tap0
ping test
#7 - NUC: Making VM with KVM

## Slide 30
$sudo apt-get install qemu-kvm libvirt-bin //upgrade KVM //qemu is open-source emulator
$wget http://old-releases.ubuntu.com/releases/16.04.4/ubuntu-16.04.4-server-amd64.iso
Install dependency & download Ubuntu 16.04.4 64bit server image.
Now we are ready to make VM. So continue the setting.
#7 - NUC: Making VM with KVM
-Install dependency to upgrade KVM

## Slide 31
Make a VM image.
Boot VM image from Ubuntu iso file (mac should be different from others).
$ sudo kvm -m 512 -name tt -smp cpus=2,maxcpus=2 -device virtio-net-pci,netdev=net0 -netdev tap,id=net0,ifname=vport_vFunction,script=no -boot d vFunction20.img -cdrom ubuntu-16.04.4-server-amd64.iso -vnc :5 -daemonize -monitor telnet:127.0.0.1:3010,server,nowait,ipv4
$sudo qemu-img create [img_name].img -f qcow2 [storage_capacity]
$sudo kvm -m [memory_capacity] -name [vm_name] -smp cpus=[#cpu],maxcpus= [#maxcpu] -device virtio-net-pci,netdev=net0,mac= [EE:EE:EE:EE:EE:EE] -netdev tap,id=net0,ifname= [tap_name],script=no -boot d [img_name].img -cdrom ubuntu-16.04.4-server-amd64.iso -vnc :[#] –daemonize -monitor telnet:127.0.0.1:3010,server,nowait,ipv4
$sudo qemu-img create vFunction20.img –f qcow2 10G
Install VNC viewer and see inside of VM
$sudo apt-get install xvnc4viewer
$xvnc4viewer localhost :5
Result..
#7 - NUC: Making VM with KVM
-Prepare for Ubuntu VM

## Slide 32
IP address:vnc number
ex) 210.203.x.x:5
#7 - NUC: Making VM with KVM
-Install Ubuntu VM

## Slide 35
public address

## Slide 37
Gateway ip of your public network

## Slide 38
Google DNS server

## Slide 39
Push Esc
$telnet localhost 3010
Trying 127.0.0.1...
Connected to localhost.Escape character is '^]'.
QEMU 0.11.0 monitor - type 'help' for more information
(qemu) eject ide1-cd0
After installing Ubuntu Linux on the VM….
You need to eject Ubuntu install image before booting to the installed OS
#7 - NUC: Making VM with KVM
- Eject Ubuntu install image

## Slide 40
If you want boot VM again (mac should be different from others).
$sudo kvm -m [memory capacity] -name [name] -smp cpus=[#cpu],maxcpus= [#maxcpu] -device virtio-net-pci,netdev=net0,mac= [EE:EE:EE:EE:EE:EE] –netdev tap,id=net0,ifname= [tap_name],script=no -boot d [name].img -vnc : [#] -daemonize
#8 - NUC: Booting VM
- VM boot command

## Slide 41
eth0
br0
ip : 0
ip : 203.237.x.x
VM
tap_name
ip : 203.237.x.x
#9 - OVS connects with KVM
- Check situation

## Slide 42
In VMs,
$sudo apt-get update
$sudo apt-get install ssh
#10 - NUC: Installing ssh in VM
- Don’t forget to install ssh in VM

## Slide 43
Docker Container connected via OVS
- Goal of this section

## Slide 44
eth0
br0
VM
Container
Tap0
ping test
#11 - Making a Docker Container

## Slide 45
$sudo wget -qO- https://get.docker.com/ | sh
$sudo systemctl start docker
$sudo adduser [Your_account] docker
(Session restart)
$sudo docker run hello-world
reference: http://docs.docker.com/linux/step_one/
Docker installation.
#11 - Making a Docker Container
- Docker installation

## Slide 46
#11 - Making a Docker Container
- Docker installation

## Slide 47
$sudo docker run -it --net=none --name [container_name] ubuntu /bin/bash
Run docker container.
I want to make interface that has 203.237.x.x IP address.
※ctrl + p, q  detach docker container
※docker attach [container_name]  get into docker container console
#11 - Making a Docker Container
- Make container

## Slide 48
eth0
br0
VM
Container
Tap0
ping test
#12 - Connect Docker Container
- Connect with OVS bridge

## Slide 49
$sudo OVS-docker add-port br0 eth0 [containerName] --ipaddress=[IP_address]/24 --gateway=[Gateway_address]
$sudo docker attach [containerName]
#apt-get update
#apt-get install net-tools
#apt-get install iputils-ping
Install OVS-docker utility in host machine. (Not in inside of Docker container.)
#12 - Connect docker Container
- Connect with OVS bridge

## Slide 50
$sudo vi /etc/rc.local
docker start [container_name]
OVS-docker del-port br0 eth0 [containerName]
OVS-docker add-port br0 eth0 [containerName] --ipaddress=[IP_address/24] --gateway=[Gateway_address]
Modify /etc/rc.local
Whenever NUC is rebooted,
network configuration of Docker container is initialized
by executing commands in rc.local
#13 – Keep Docker network configuration
- /etc/rc.local

## Slide 51
eth0
br0
VM
Container
Tap0
ping test
#14 – Check connectivity: VM & Container

## Slide 52
#14 - Check connectivity: VM & Container
-Check connectivity with ping command

## Slide 53
KVM VM
Docker container
#14 - Check connectivity: VM & Container
-Check connectivity with ping command

## Slide 54
VM
Box Lab: Final Goal (Recap)

## Slide 55
Lab Review

## Slide 56
Lab Summary
With Box Lab, you have experimented
How to install and configure Linux OS into Box (i.e., computer).
How to install and configure OVS (Open vSwitch) virtual switch inside a Linux Box and configure it.
How to create VMs and Docker containers inside a Linux Box and then inter-connect each of them together and to the Internet.

## Slide 57
Thank You for Your Attention
Any Questions?
mini@smartx.kr