## Slide 1
https://github.com/SmartX-Labs/SmartX-Mini-MOOC
Lab #1: Box
Computer Systems
For AI-inspired Cloud
Theory & Lab.

## Slide 2
Box Lab: Outline
eno1
br0
VM
Container
Tap1
ping test

## Slide 3
VM
Box Lab: Final Goal

## Slide 4
The keyboard means that you should execute instructions by following the guidance.
Lab Theory
Lab
Practice
Lectures are divided into Lab Theory, Lab Practice and Lab Review parts.
Lab
Review
Before you start
- Things you need to know

## Slide 5
Lab Theory

## Slide 6
eno1
br0
VM
Container
Tap1
ping test
Linux Box with Virtualization/Containers
Virtual Machine
&
Container
Linux Box

## Slide 7
Virtual Machines (VMs)
Heavier than
Container!
Hypervisor Tool for creating VMs
On a Linux Box (e.g., NUC)
Multiple fully-isolated (with dedicated resources), but heavy VM instances (i.e., VMs).
Multiple partially-isolated, lightweight container instances (i.e., containers)
VMs and Containers on a Linux Box
Containers
Container Runtime Tool for running containers

## Slide 8
eno1
br0
VM
Container
Tap1
ping test
A Switch inside Linux Box: Open vSwitch

## Slide 9
Hypervisor
VM
Virtual switch
VM
VM
VM
Physical switch
Virtual NIC
Virtual interface
Virtual L2 network
Linux Box
L2 network
A software-based virtual switch allows one VM to communicate with neighbor VMs as well as to connect to Internet (via physical switch).
Software-based switches (running with the power of CPUs) are known to be more flexible/upgradable and benefited of virtualization (memory overcommit, page sharing, …)
VMs (similarly containers) have logical (virtual) NIC with virtual Ethernet ports so that they can be plugged into the virtual interface (port) of virtual switches.
Virtual Switch in a Box to connect VMs

## Slide 10
http://openvswitch.org/
Open vSwitch is an open-source virtual switch software designed for virtual servers.
OVS Main components
Linux-adopted virtual switch: Open vSwitch

## Slide 11
Lab Practice

## Slide 12: NAME: NUC5i5MYHE (NUC PC) CPU: Intel® Core™ i3-8109U 3.60 GHz CORE: 2 Memory: 32GB DDR4 HDD: 94GB
#0 - Lab Preparation
Wired connection
NAME: Raspberry Pi Model B (Pi) CPU: ARM Cortex A7 @900MHz CORE: 4 Memory: 1GB SD Card: 32GB
NAME: netgear prosafe 16 port gigabit switch(Switch) Network Ports: 16 auto-sensing 10/100/1000 Mbps Ethernet ports
NAME: NT900X3A
CPU: i5-2537U @1.40GHz
CORE: 2 Memory: 4GB DDR3 HDD: 128GB

## Slide 13
OS : Ubuntu Desktop 20.04 LTS(64bit)
  Download Site : https://releases.ubuntu.com/20.04/
    Installed on NUC
Ubuntu Home Screen After Installation
#1 - NUC: OS Installation

## Slide 14
#1 - NUC: OS Installation
- OS Installation
Updates and other software
Select ‘Minimal installation’
Installation type
Select ‘Something else’
On /dev/sda or /dev/nvme0n1
  (UEFI), add 512MB EFI partition
  Add empty partition with 20GB (20480MB) (Select ‘do not use the partition’)
  Add Etc4 partition on leave memory
Select Boot loader
  BIOS: Ext4 partition
  UEFI: EFI partition
LVM관련 오류 발생 시
뒤로 이동하여 Installation type화면으로 이동
Erase disk 선택
시간대 선택화면까지 진행
다시 뒤로 돌아가서 다시 Installation type화면으로 이동
Something else선택 후 정상 진행

## Slide 15
eno1
br0
VM
Container
Tap1
ping test
#2 - NUC: Network Configuration

## Slide 16
#2 - NUC: Network Configuration
- ‘Temporary’ Network Configuration using GUI
eno1
br0
VM
Container
Tap1
ping test

## Slide 17
#2 - NUC: Network Configuration
- ‘Temporary’ Network Configuration using GUI
Click the LAN configuration icon.
Enter the network info.
(IP address, subnet mask, gateway)

## Slide 18
#2 - NUC: Network Configuration
- Set Prerequisites
$sudo apt update
$sudo apt upgrade
0. Update & Upgrade
$sudo apt install net-tools ifupdown
$ifconfig -a
1. Install net-tools & ifupdown

## Slide 19
#2 - NUC: Network Configuration
- Set Prerequisites
$sudo apt intall openvswitch-switch
$sudo ovs-vsctl add-br br0
$sudo ovs-vsctl show
2. Install openvswitch-switch & make br0 bridge
ovs-vsctl show

## Slide 20
#2 - NUC: Network Configuration
- Network interface
eno1
br0
VM
Container
Tap1
ping test

## Slide 21
#2 - NUC: Network Configuration
- Network interface
$sudo su
#systemctl stop systemd-networkd.socket systemd-networkd networkd-dispatcher \
systemd-networkd-wait-online
#systemctl disable systemd-networkd.socket systemd-networkd networkd-dispatcher \
systemd-networkd-wait-online
#systemctl mask systemd-networkd.socket systemd-networkd networkd-dispatcher \
systemd-networkd-wait-online
#apt-get --assume-yes purge nplan netplan.io
#exit
Disable netplan

## Slide 22
#2 - NUC: Network Configuration (1/3)
- eno1 interface
$sudo vi /etc/systemd/resolved.conf
----------------- /etc/systemd/resolved.conf -----------------
…
DNS = 8.8.8.8 8.8.4.4
…
----------------------------------------------------------------------------
$sudo systemctl restart systemd-resolved.service
$sudo ifup eno1
NUC internet works!
Your Box
eno1
<Your IP addr>

## Slide 23
#2 - NUC: Network Configuration
- Network interface
Open /etc/network/interfaces via 'vi'
$sudo vi /etc/network/interfaces
----------------- /etc/network/interfaces -----------------
auto lo
iface lo inet loopback
auto br0
iface br0 inet static
address <your nuc ip>
netmask 255.255.255.0
gateway <gateway ip>
dns-nameservers 8.8.8.8
auto eno1
iface eno1 inet manual
auto vport_vFunction
iface vport_vFunction inet manual
pre-up ip tuntap add vport_vFunction mode tap
up ip link set dev vport_vFunction up
post-down ip link del dev vport_vFunction
----------------------------------------------------------------------------
Configurate the Network Interface vport_vFunction is a tap interface and attach it to your VM.
Some NUC have different Interface name.
So you need to check your NUC’s interface name using
‘ip a’ command.

## Slide 24
#2 - NUC: Network Configuration
- Network interface
Your Box
eno1
---your nuc ip---
br0
---your nuc ip---
VM
---your vm ip---
vport_vFunction
[tap_name]
We will make VM attaching vport_vFunction. You can think this tap as a NIC of VM.
Below is the figure you configurated so far

## Slide 25
#2 - NUC: Network Configuration
- Network interface
$sudo ovs-vsctl add-port br0 eno1
$sudo ovs-vsctl add-port br0 vport_vFunction
$sudo ovs-vsctl show
add port ‘eno1’ and ‘vport_vFunction’ to ‘br0’
#systemctl unmask networking
#systemctl enable networking
#systemctl restart networking
#exit
Restrart the whole interfaces 2
$sudo su
#systemctl unmask networking
#systemctl enable networking
#systemctl restart networking
Restrart the whole interfaces 1

## Slide 26
VM
KVM-based VM connected via OVS
- Goal of this section

## Slide 27
eno1
br0
VM
Container
Tap0
ping test
#3 - NUC: Making VM with KVM
[Tap_name]
vport_vFunction

## Slide 28
$sudo apt install qemu-kvm libvirt-daemon-system libvirt-clients bridge-utils
//upgrade KVM
//qemu is open-source emulator
$wget http://old-releases.ubuntu.com/releases/focal/ubuntu-20.04-beta-live-server-amd64.iso
Install dependency & download Ubuntu 20.04 64bit server image.
Now we are ready to make VM. So, continue the setting.
#3 - NUC: Making VM with KVM
-Install dependency to upgrade KVM

## Slide 29
Make a VM image.
Boot VM image from Ubuntu iso file (띄어쓰기 주의!).
$ sudo kvm -m 1024 -name tt -smp cpus=2,maxcpus=2 -device virtio-net-pci,netdev=net0 -netdev tap,id=net0,ifname=vport_vFunction,script=no -boot d vFunction20.img -cdrom ubuntu-20.04-beta-live-server-amd64.iso -vnc :5 -daemonize -monitor telnet:127.0.0.1:3010,server,nowait,ipv4
$sudo qemu-img create [img_name].img -f qcow2 [storage_capacity]
$sudo kvm -m [memory_capacity] -name [vm_name] \
-smp cpus=[#cpu],maxcpus= [#maxcpu] \
-device virtio-net-pci,netdev=net0 \
-netdev tap,id=net0,ifname= [tap_name],script=no \
-boot d [img_name].img \
-cdrom ubuntu-20.04-beta-live-server-amd64.iso -vnc :[#] \
-daemonize -monitor telnet:127.0.0.1:3010,server,nowait,ipv4
$sudo qemu-img create vFunction20.img -f qcow2 10G
#3 - NUC: Making VM with KVM
-Prepare for Ubuntu VM

## Slide 30
#3 - NUC: Making VM with KVM
-Prepare for Ubuntu VM
$sudo iptables –A FORWARD –i eno1 –j ACCEPT
$sudo iptables –A FORWARD –o eno1 –j ACCEPT
$sudo iptables –t nat –A POSTROUTING –s 192.168.100.0/24 –o eno1 –j SNAT --to <Your ip address>
Configure SNAT with iptables for VM network
$sysctl –p
net.ipv4.ip_forward = 1
$vi /etc/sysctl.conf
#net.ipv4.ip_forward=1
net.ipv4.ip_forward=1
Configuration complete

## Slide 31
#3 - NUC: Making VM with KVM
-Install Ubuntu VM (control with ‘Enter key’ and ‘Arrow keys’)
Install VNC viewer and see inside of VM
$sudo apt-get install tigervnc-viewer
$vncviewer localhost:5
If ok, you can see window like this

## Slide 32
#3 - NUC: Making VM with KVM
- VM network configuration (control with ‘Enter key’ and ‘Arrow keys’)
네트워크 디바이스 선택 -> Edit IPv4
IPv4 Method -> Manual
설정
subnet: 203.237.53.0/24
Address: <your vm ip>
Gateway: <gateway ip>
Name Servers: 8.8.8.8
1. Select network device ‘Edit IPv4’
2. Select ‘Manual’
3. Enter the network info.

## Slide 33
#3 - NUC: Making VM with KVM
- Installation Completed (control with ‘Enter key’ and ‘Arrow keys’)
When ‘installation completed’ message is shown, terminate the VM
$ sudo killall -9 qemu-system-x86_64
boot VM again (mac should be different from others).
$ sudo kvm -m 1024 -name tt -smp cpus=2,maxcpus=2 -device virtio-net-pci,netdev=net0 -netdev tap,id=net0,ifname=vport_vFunction,script=no -boot d vFunction20.img -vnc :5 -daemonize
$sudo kvm -m [memory_capacity] -name [vm_name] \
-smp cpus=[#cpu],maxcpus= [#maxcpu] \
-device virtio-net-pci,netdev=net0 \
-netdev tap,id=net0,ifname= [tap_name],script=no \
-boot d [img_name].img \
-daemonize

## Slide 34
eno1
br0
ip : ---your nuc ip---
ip : ---your nuc ip---
VM
tap_name
ip : ---your vm ip---
#5 - OVS connects with KVM
- Check situation

## Slide 35
In VMs,
$sudo apt update
$sudo apt -y install net-tools ssh
#6 - NUC: Installing ssh in VM
- Don’t forget to install ssh in VM

## Slide 36
Docker Container connected via OVS
- Goal of this section

## Slide 37
eno1
br0
VM
Container
Tap0
ping test
#7 - Making a Docker Container

## Slide 38
// Set up the repository:
// Install packages to allow apt to use a repository over HTTPS
$ sudo apt-get update
$ sudo apt-get install -y ca-certificates curl gnupg lsb-release
// Add Docker's official GPG key:
$ curl -fsSL https://download.docker.com/linux/ubuntu/gpg | sudo gpg --dearmor -o /usr/share/keyrings/docker-archive-keyring.gpg
// Add the Docker apt repository:
$ echo \
"deb [arch=$(dpkg --print-architecture) signed-by=/usr/share/keyrings/docker-archive-keyring.gpg] https://download.docker.com/linux/ubuntu \
$(lsb_release -cs) stable" | sudo tee /etc/apt/sources.list.d/docker.list > /dev/null
// Install Docker CE
$ sudo apt-get update
$ sudo apt-get install docker-ce docker-ce-cli containerd.io
// Create /etc/docker
$ sudo mkdir -p /etc/docker
In NUC, Docker installation.(Based on Docker Documentation link)
#7 - Making a Docker Container
- Docker installation
cont‘d on next page

## Slide 39
Docker installation (cont’d)
#7 - Making a Docker Container
- Docker installation
In NUC,
//continued
// Set up the Docker daemon
$ cat <<EOF | sudo tee /etc/docker/daemon.json
{
"exec-opts": ["native.cgroupdriver=systemd"],
"log-driver": "json-file",
"log-opts": {
"max-size": "100m"
},
"storage-driver": "overlay2"
}
EOF
// Create /etc/systemd/system/docker.service.d
$ sudo mkdir -p /etc/systemd/system/docker.service.d
$ sudo systemctl daemon-reload
$ sudo systemctl enable docker
$ sudo systemctl restart docker
$ sudo systemctl restart docker.socket

## Slide 40
$ sudo docker run hello-world
reference: http://docs.docker.com/linux/step_one/
Now Installation completed. Let's Check it
#7 - Making a Docker Container
- Docker installation
In NUC,

## Slide 41
$sudo docker run -it --net=none --name [container_name] ubuntu /bin/bash
Run docker container. (**Remember the container_name)
※ctrl + p, q  detach docker container
※docker attach [container_name]  get into docker container console
#7 - Making a Docker Container
- Make container

## Slide 42
eno1
br0
VM
Container
Tap0
ping test
#8 - Connect Docker Container
- Connect with OVS bridge

## Slide 43
$sudo ovs-docker add-port br0 veno1 [container_name] --ipaddress=---your docker ip---/24 \
--gateway=---gateway ip---
$sudo docker attach [container_name] //enter to docker container
#apt update
#apt install net-tools
#apt install iputils-ping
Install OVS-docker utility in host machine. (Not in inside of Docker container.)
#8 - Connect docker Container
- Connect with OVS bridge

## Slide 44
$sudo vi /etc/rc.local
#!/bin/bash
docker start [container_name]
ovs-docker del-port br0 veno1 [containerName]
ovs-docker add-port br0 veno1 [container_name] --ipaddress=---your docker ip---/24 --gateway=---gateway ip---
Modify /etc/rc.local
Whenever NUC is rebooted,
network configuration of Docker container is initialized
by executing commands in rc.local
#9 – Keep Docker network configuration
- /etc/rc.local

## Slide 45
eno1
br0
VM
Container
Tap0
ping test
#10 – Check connectivity: VM & Container

## Slide 46
#10 - Check connectivity: VM & Container
-Check connectivity with ping command

## Slide 47
KVM VM
Docker container
#10 - Check connectivity: VM & Container
-Check connectivity with ping command

## Slide 48
VM
Box Lab: Final Goal (Recap)

## Slide 49
Lab Review

## Slide 50
Lab Summary
With Box Lab, you have experimented
How to install and configure Linux OS into Box (i.e., computer).
How to install and configure OVS (Open vSwitch) virtual switch inside a Linux Box and configure it.
How to create VMs and Docker containers inside a Linux Box and then inter-connect each of them together and to the Internet.

## Slide 51
Thank You for Your Attention
Any Questions?
mini@smartx.kr